## Slide 1
GROUND TRUTH SYSTEM DATA WORKFLOW OVERVIEW
From the Cabin to Usable Data
How vehicle in-cabin data is collected, labelled, uploaded to the cloud and used to measure KPIs and train algorithms
22 October 2026

## Slide 2
The Life Of The Data
Four stages turn what happens in the cabin into labelled data in the cloud, ready to be used.
Ground Truth System Data Workflow Overview
2 / 6
Collect
Capture every data source on one timeline and record each session
capture · synchronise · record
1
Label
Add the context and the ground truth that make the data usable
recording labels · frame labels
2
Upload
Bundle each recording with its labels and send it to the cloud
package · upload to database
3
Use
Measure KPIs and train algorithms with the labelled data
measure KPIs · train algorithms
4
Why does the data matter?
The device under test/development is an in-cabin camera system that monitors a car driver’s alertness level.
Labelled recordings show how well it performs today, and they are what tomorrow's algorithms learn from.

## Slide 3
Collect: Many Sources, One Timeline
1 · Collect
2 · Label
3 · Upload
4 · Use
Ground Truth System Data Workflow Overview
3 / 6
WHAT WE CAPTURE
Reference cameras
High-quality views of the driver from multiple angles
Device under test
Its own camera, plus what algorithm detects, such as gaze, alertness level
Scene camera
An ordinary camera that films the whole scene
Motion capture
Tracks the position and rotation of the driver's head precisely
Driver vital signs
Heart rate, breathing rate, blood pressure, alcohol level and more
From signals to a recording
Translate. A small adapter program per source converts its data into one common format and checks data validity.
Time-stamp. Every frame and measurement gets a time from one shared clock, so all sources line up.
Count. Frames are numbered, so missing frames can be spotted.
Watch. Operators check the live streams, so problems are caught during the session.
Record. Every stream is saved in full, in one recording per session.
Result: one complete recording per session, with every stream on the same timeline.

## Slide 4
Label: Make The Data Usable
1 · Collect
2 · Label
3 · Upload
4 · Use
Ground Truth System Data Workflow Overview
4 / 6
Labels for the whole recording
Who and what was recorded, and under which conditions
Scenario: what the driver does, e.g., with certain task
Environmental conditions and seating position
People on board, e.g., glasses, beard, headgear
Project information and hardware setup, e.g., cameras and sensors used
Written into one description file per recording and checked by validation tools.
Labels for every frame: the ground truth
The right answers that the device is measured against and algorithms learn from
Where the driver looks
Position and rotation of the head
Eye opening and eye state
Vital status
From reference sensors such as motion capture and gaze targets, automatic labelling and manual annotation.
Result: every recording carries its context and its right answers, so it can be found, compared and learned from.

## Slide 5
Upload: Send The Data To The Cloud
1 · Collect
2 · Label
3 · Upload
4 · Use
Ground Truth System Data Workflow Overview
5 / 6
Package
Bundle everything about one recording into one archive:
the recording itself
its labels and annotations
calibration data
logs
The archive is named by the recording's fingerprint (hash), so the cloud can recognise it.
Upload to database on cloud
An upload tool sends the archive to the cloud recording database:
Sign in with an access key.
Look up the fingerprint: not to store twice.
Create a new entry, together with the recording's labels.
Check that the upload is complete.
Result: each recording becomes one entry in the database, stored together with its labels and ready to be used.

## Slide 6
Use: Measure KPIs And Train Algorithms
1 · Collect
2 · Label
3 · Upload
4 · Use
Ground Truth System Data Workflow Overview
6 / 6
Measure KPIs
KPI tool lines up the device's results with the ground truth, frame by frame, and measures the differences.
Availability: when the ground truth has a value, how often does the device give a valid one too?
Accuracy: how far off is it?
Example: eye opening left eye, one sample recording, test run
87 %
valid where the ground truth has a value
1.5 mm
mean absolute error
Train algorithms
The same labelled recordings are the raw material for new perception algorithms.
Training data: the ground truth gives the right answer for every frame.
Test data: recordings kept aside check the result with the same KPIs.
The right mix: labels such as scenario, lighting or glasses help pick balanced data.
The big picture: collect → label → upload → use. Labelled data measures today's system and trains tomorrow's algorithms.